TENDER SPECIFICATIONS

The Radar Unit “ERA” consists of:

Interface unit:

It contains the display and the radar control system.

Display unit:

High definition 6” rectangular monochrome LCD display.

Display resolution: 240 x 320 pixels.

Markers: Heading Line, Bearing Scale, Range Rings, Variable Range Marker (VRM), Electronic Bearing Line (EBL), Tuning Bar, Cursor, Parallel Cursor, Alarm Zone, Waypoint Mark*, North Mark*.

Alphanumeric indications: Range, Range Ring Interval, Display Mode (HU), Interference Rejection (IR), Variable Range Marker (VRM), Electronic Bearing Line (EBL), Stand-By (ST-BY), Guard Alarm (G (IN), G (OUT), UP RANGE), Echo Stretch (ES), Range and Bearing to Cursor, Bearing or L/L Position, Echo Tailing (TRAIL), Trailing Time, Trailing Elapsed Time, Watchman (WATCHMAN),

Zoomed Display (ZOOM), Navigation Data*, Heading* (HDC).

*:external data required.

Battery system:

Battery charger (included inside the interface unit).

Battery: nominal voltage: 12 VDC, capacity: 24 AH.

Connector to the GPS module.

Connector to the Radar Antenna.

Radar Antenna:

Outdoor operation.

Directional antenna: Micro-strip patch array antenna.

Horizontal polarization.

Frequency 9.4 GHz (X-band).

Antenna rotation speed 24/31/41 rpm nominal (auto-select according to range).

Horizontal Beamwidth less than 6.2°. Vertical Beamwidth 25°.

Connection cable to the interface unit.

GPS module:

High contrast display with gray scale. Display resolution: 120 x 160 pixels.

GPS Accuracy: 15 m. DGPS (WAAS) Accuracy: 3 m.

Connection cable to the interface unit.

Extendable tripod stand:

Telescopic tripod stand, of anodized aluminum, to hold the radar antenna at the appropriate height. It includes a bull's eye level indicator. Operation range: 1.20 m – 3.05 m. Maximum supported weight: 7.5 kg.

Mobile cart:

Mobile cart to hold the elements of the ERA unit. It incorporates wheels (strong tires) to facilitate its mobility and the operation in uneven grounds.

Cables and Accessories, for normal operation.

Manuals:

This unit is supplied with the following manuals: Required Services, Assembly and Installation, Starting-up, Safety, Maintenance & Practices Manuals.

- Dimensions: 600 x 900 x 1700 mm approx. (23.62 x 35.43 x 66.93 inches approx.). - Weight: 50 Kg approx. (110 pounds approx.).

EXERCISES AND PRACTICAL POSSIBILITIES

1.- Familiarization with the unit.

2.- Establish communication with GPS module.

3.- Configuration of the radar range.

4.- Sensitivity adjustment.

5.- Range measurement.

6.- Bearing measurement.

7.- Setting of the suppressing interference function.

8.- Setting of the suppressing rain clutter function.

9.- Analysis of the guard alarm function and establish a guard zone.

10.- Analysis of the watchman function.

Optional

ERA/ICAI. Interactive Computer Aided Instruction Software:

This complete software package consists of an Instructor Software (EDIBON Classroom Manager - ECM-SOF) totally integrated with the Student Software (EDIBON Student Labsoft - ESL-SOF). Both are interconnected so that the teacher knows at any moment what is the theoretical and practical knowledge of the students.

- ECM-SOF. EDIBON Classroom Manager (Instructor Software).

ECM-SOF is the application that allows the Instructor to register students, manage and assign tasks for workgroups, create own content to carry out Practical Exercises, choose one of the evaluation methods to check the Student knowledge and monitor the progression related to the planned tasks for individual students, workgroups, units, etc... so the teacher can know in real time the level of understanding of any student in the classroom.

Innovative features:

• User Data Base Management.

• Administration and assignment of Workgroup, Task and Training sessions.

• Creation and Integration of Practical Exercises and Multimedia Resources.

• Custom Design of Evaluation Methods.

• Creation and assignment of Formulas & Equations.

• Equation System Solver Engine.

• Updatable Contents.

• Report generation, User Progression Monitoring and Statistics.

- ESL-SOF. EDIBON Student Labsoft (Student Software).

ESL-SOF is the application addressed to the Students that helps them to understand theoretical concepts by means of practical exercises and to prove their knowledge and progression by performing tests and calculations in addition to Multimedia Resources. Default planned tasks and an Open workgroup are provided by EDIBON to allow the students start working from the first session. Reports and statistics are available to know their progression at any time, as well as explanations for every exercise to reinforce the theoretically acquired  technical knowledge.

Innovative features:

• Student Log-In & Self-Registration.

• Existing Tasks checking & Monitoring.

• Default contents & scheduled tasks available to be used from the first session.

• Practical Exercises accomplishment by following the Manual provided by EDIBON.

• Evaluation Methods to prove your knowledge and progression.

• Test self-correction.

• Calculations computing and plotting.

• Equation System Solver Engine.

• User Monitoring Learning & Printable Reports.

• Multimedia-Supported auxiliary resources.