TENDER SPECIFICATIONS

U-shape frame to mount the piping.

The unit includes wheels to facilitate its mobility.

Diagram in the front panel with distribution of the elements similar to the real one.

Pipe circuit formed by tubes, bends, T-shaped pieces and reducers (DN15, DN25 and DN40).

Pressure vessel with manometer:

DN15 connector for PN16.

Manometer, range: 0 – 10 bar.

Connecting elements:

Types: flange and cutting ring screw fitting.

Sizes: DN40, DN25, DN15 and G½”.

Set of valves and accessories made of stainless steel and cast iron:

Gate valve: DN40 for PN16.

Four bellows valves: DN15 and DN25 for PN16.

Three ball valves: DN40 and DN15 for PN16.

Three ball valves with cutting ring screw fitting in G½”.

Condensate drain: DN25 for PN16.

Sight glass: DN15 for PN25.

Two check valve: DN15 for PN16.

Flanged filter in DN15 for PN16.

Conical seat valve: DN25 for PN16.

Two manometers, range: 0 – 10 bar.

Set of tools.

Ladder.

Cables and accessories, for normal operation.

Manuals: This unit is supplied with the following manuals: Required services, Assembly and Installation, Starting-up, Safety, Maintenance & Practices manuals.

Additional recommended elements (Not included):

- PVFA/AA. Unit for Assembly and Alignment of Pumps and Driving Motor.

Anodized aluminum frame and panels made of painted steel.

Diagram in the front panel with distribution of the elements similar to the real one.

Centrifugal pump: 580  l/min; 18.8 m.

Single-phase motor.

Storage tank, volume: 140  l.

Manometer, range: 0 – 10  bar.

- Dimensions: 1500 x 2000 x 2000 mm approx. (59.05 x 78.74 x 78.74 inches approx.) - Weight: 280 Kg approx. (617 pounds approx.)

EXERCISES AND PRACTICAL POSSIBILITIES

1.- Principles and main elements of a hydraulic system.

2.- Construction and operation of fittings and valves, pipes and system accessories.

3.- Design of diagrams and planning of installations according to requirements.

4.- Selection of elements and material required for the assembly.

5.- Assembly of the installation in accordance to the diagram.

6.- Understanding and interpretation of industrial diagrams and associated technical documentation.

7.- Start up and operation of the constructed system (required PVFA/AA accessory).

Optional

PVFA/ICAI. Interactive Computer Aided Instruction Software:

This complete software package consists of an Instructor Software (EDIBON Classroom Manager - ECM-SOF) totally integrated with the Student Software (EDIBON Student Labsoft - ESL-SOF). Both are interconnected so that the teacher knows at any moment what is the theoretical and practical knowledge of the students.

- ECM-SOF. EDIBON Classroom Manager (Instructor Software).

ECM-SOF is the application that allows the Instructor to register students, manage and assign tasks for workgroups, create own content to carry out Practical Exercises, choose one of the evaluation methods to check the Student knowledge and monitor the progression related to the planned tasks for individual students, workgroups, units, etc... so the teacher can know in real time the level of understanding of any student in the classroom.

Innovative features:

• User Data Base Management.

• Administration and assignment of Workgroup, Task and Training sessions.

• Creation and Integration of Practical Exercises and Multimedia Resources.

• Custom Design of Evaluation Methods.

• Creation and assignment of Formulas & Equations.

• Equation System Solver Engine.

• Updatable Contents.

• Report generation, User Progression Monitoring and Statistics.

- ESL-SOF. EDIBON Student Labsoft (Student Software).

ESL-SOF is the application addressed to the Students that helps them to understand theoretical concepts by means of practical exercises and to prove their knowledge and progression by performing tests and calculations in addition to Multimedia Resources. Default planned tasks and an Open workgroup are provided by EDIBON to allow the students start working from the first session. Reports and statistics are available to know their progression at any time, as well as explanations for every exercise to reinforce the theoretically acquired  technical knowledge.

Innovative features:

• Student Log-In & Self-Registration.

• Existing Tasks checking & Monitoring.

• Default contents & scheduled tasks available to be used from the first session.

• Practical Exercises accomplishment by following the Manual provided by EDIBON.

• Evaluation Methods to prove your knowledge and progression.

• Test self-correction.

• Calculations computing and plotting.

• Equation System Solver Engine.

• User Monitoring Learning & Printable Reports.

• Multimedia-Supported auxiliary resources.