TENDER SPECIFICATIONS

Bench-top unit.

Anodized aluminum frame and panels made of painted steel.

Main metallic elements made of stainless steel.

Diagram in the front panel with distribution of the elements similar to the real one.

Dead-weight calibrator:

Diameter of the piston: 18 mm.

Two area of the piston: 0.000254469 m.

Weight of the piston: 0.5 Kg.

It uses water for safety and ease of use purposes.

Set of weights:

0.5 Kg, 1 Kg, 2.5 Kg, 5 Kg.

Bourdon type manometer, connected to the dead weight calibrator, range: 0 – 2.5 bar (250 kN/m² ), class: 1.6. It includes a scale calibrated in degrees of rotation, apart from the usual pressure scale.

Electronic pressure sensor, connected to the dead weight calibrator, range: 0 – 2.5 bar (250 kN/m² ).

Vessel, made of PMMA, to facilitate the priming of the calibrator.

Electronic console with two digital displays that show the output of the pressure sensor (in Volts) and the conditioned reading in two engineering units (kN/m²). Besides the corresponding signals are sent to an I/O port for their acquisition via software in a computer (PC).

Electronic console:

Metallic box.

Main switch.

Pressure sensor connection.

Digital display for the pressure sensor (in kN/m).

Digital display for the pressure sensor (in Volts).

Connection to computer (PC).

Software to acquire data and to obtain the calibration curve (with slope and ordinate in the origin) both in function of the angular displacement of the needle and in function of the output voltage of the sensor.

Cables and Accessories, for normal operation.

Manuals: This unit is supplied with the following manuals: Required Services, Assembly and Installation, Starting-up, Safety, Maintenance & Practices Manuals.

Unit: - Dimensions: 500 x 350 x 350 mm approx. (19.68 x 13.78 x 13.78 inches approx.) - Weight: 15 Kg approx.  (33 pounds approx.)

Electronic console: - Dimensions: 310 x 220 x 145 mm approx. (12.20 x 8.66 x 5.70 inches approx.) - Weight:  3 Kg approx. (6.6 pounds approx.)

EXERCISES AND PRACTICAL POSSIBILITIES

1.- Study of the concept of pressure (force/area).

2.- Study of the function of a dead-weight pressure calibrator.

3.- Study of the concepts of measurement and calibration (gauge and absolute pressures, zero error, non-linearity, scale error, conversion of arbitrary scale into engineering units).

4.- Study of pressure scales.

5.- Study of the operation and characteristic behaviour of a Bourdon type manometer.

6.- Checking the readings of a Bourdon type manometer using a standard set of calibrated weights.

7.- Calibration of a Bourdon type manometer in engineering two units (kN/m² ).

8.- Calibration of a Bourdon type manometer in arbitrary units (angular displacement of needle).

9.- Study of the operation and characteristic behaviour of a pressure sensor.

10-  Calibration of a pressure sensor (output voltage of the sensor).

11.- Calibration of a pressure sensor and signal conditioning circuit in engineering units.

12.- Study of the sources of error in measuring and calibration (signal conditioning, manufacturing tolerances, display resolution, friction and backlash…).

Optional

TMCP/ICAI. Interactive Computer Aided Instruction Software:

This complete software package consists of an Instructor Software (EDIBON Classroom Manager - ECM-SOF) totally integrated with the Student Software (EDIBON Student Labsoft - ESL-SOF). Both are interconnected so that the teacher knows at any moment what is the theoretical and practical knowledge of the students.

- ECM-SOF. EDIBON Classroom Manager (Instructor Software).

ECM-SOF is the application that allows the Instructor to register students, manage and assign tasks for workgroups, create own content to carry out Practical Exercises, choose one of the evaluation methods to check the Student knowledge and monitor the progression related to the planned tasks for individual students, workgroups, units, etc... so the teacher can know in real time the level of understanding of any student in the classroom.

Innovative features:

• User Data Base Management.

• Administration and assignment of Workgroup, Task and Training sessions.

• Creation and Integration of Practical Exercises and Multimedia Resources.

• Custom Design of Evaluation Methods.

• Creation and assignment of Formulas & Equations.

• Equation System Solver Engine.

• Updatable Contents.

• Report generation, User Progression Monitoring and Statistics.

- ESL-SOF. EDIBON Student Labsoft (Student Software).

ESL-SOF is the application addressed to the Students that helps them to understand theoretical concepts by means of practical exercises and to prove their knowledge and progression by performing tests and calculations in addition to Multimedia Resources. Default planned tasks and an Open workgroup are provided by EDIBON to allow the students start working from the first session. Reports and statistics are available to know their progression at any time, as well as explanations for every exercise to reinforce the theoretically acquired  technical knowledge.

Innovative features:

• Student Log-In & Self-Registration.

• Existing Tasks checking & Monitoring.

• Default contents & scheduled tasks available to be used from the first session.

• Practical Exercises accomplishment by following the Manual provided by EDIBON.

• Evaluation Methods to prove your knowledge and progression.

• Test self-correction.

• Calculations computing and plotting.

• Equation System Solver Engine.

• User Monitoring Learning & Printable Reports.

• Multimedia-Supported auxiliary resources.