TENDER SPECIFICATIONS

The application “AEL-DCGEA” includes the following elements:

• N-ALI02. Domestic Main Power Supply Module.

Supply voltage (single-phase): 230 VAC, 1PH + N.

ON / OFF removable key.

Output voltage connections:

Two single-phase: 230 VAC.

Single-shase supply hose connecting plug.

Differential magnetothermal, 2 poles, 25 A, 30 mA AC, 6 KA.

Emergency stop push-button.

• N-VVCC/M. DC Motors Speed Controller (Intermediate option).

Supply voltage: 230 VAC.

Variable output voltage: 0 – 300 VDC.

Fuse: 2 A.

• N-REV. Single-Phase Variable Resistor Module.

Variable resistor: 150 Ohm.

Maximum power: 500 W.

Potentiometer.

Terminals:

Three terminals to choose all resistance or variable resistance.

Fuse: 2 A.

• N-REF. Single-Phase Fixed Resistor Module.

Resistor value: 150 Ohm.

Maximum power: 500 W.

Selector:

Position 0: Circuit opened.

Position 1: Circuit closed.

Fuse: 2 A.

• EMT1. DC Independent Excitation Motor-Generator.

Nominal power: 250 W.

Armature voltage: 200 VDC.

Excitation voltage: 190 VDC.

Armature current: 1.5 A.

Excitation current: 0.3 A.

Speed: 3000 rpm.

Shaft height: 71 mm.

• N-VVCA/M. AC Motors Speed Controller Module (intermediate option).

ON / OFF Switch.

Supply voltage: 230 VAC.

Nominal power: 750 W.

PWM output voltage connections:

Three-phases: 230 VAC.

10 K, potentiometer for the induction motor control speed.

Setting and visualization display of the machine parameters.

• EMT7. 3PH Squirrel-Cage Motor.

Nominal power: 370 W.

Nominal voltage: 3 x 230 / 400 VAC Δ/Y.

Frequency: 50 / 60 Hz.

Number of poles: 2.

Speed: 2730 rpm.

Nominal current: 1.67 / 0.97 A.

Shaft height: 71 mm.

Additional recommended elements (Not included):

• N-MED17. DC Voltmeter Module (0-200 V) (2 units).

Measurement range: 0 – 200 VDC.

Terminals:

Measurement terminals.

• N-MED05. DC Ammeter Module (0-1.5 A) (2 units).

Measurement range: 0 – 200 VDC.

Terminals:

Measurement terminals.

• All necessary cables to realize the practical exercises are included.

Cables and accessories, for normal operation.

Manuals:

This unit is supplied with the following manuals: Required services, Assembly and Installation, Starting-up, Safety, Maintenance & Practices manuals.

- Dimensions: 640 x 320 x 670 mm approx. (25.19 x 12.59 x 26.32 inches approx.) - Weight: 35 Kg approx. (77 pounds approx.)

EXERCISES AND PRACTICAL POSSIBILITIES

1.- Control of generated voltage.

2.- Control of the excitation of the DC generator.

3.- Driving motor speed variation.

4.- Loading of the DC generator.

Optional

AEL-DCGEA/ICAI. Interactive Computer Aided Instruction Software:

This complete software package consists of an Instructor Software (EDIBON Classroom Manager - ECM-SOF) totally integrated with the Student Software (EDIBON Student Labsoft - ESL-SOF). Both are interconnected so that the teacher knows at any moment what is the theoretical and practical knowledge of the students.

- ECM-SOF. EDIBON Classroom Manager (Instructor Software).

ECM-SOF is the application that allows the Instructor to register students, manage and assign tasks for workgroups, create own content to carry out Practical Exercises, choose one of the evaluation methods to check the Student knowledge and monitor the progression related to the planned tasks for individual students, workgroups, units, etc... so the teacher can know in real time the level of understanding of any student in the classroom.

Innovative features:

• User Data Base Management.

• Administration and assignment of Workgroup, Task and Training sessions.

• Creation and Integration of Practical Exercises and Multimedia Resources.

• Custom Design of Evaluation Methods.

• Creation and assignment of Formulas & Equations.

• Equation System Solver Engine.

• Updatable Contents.

• Report generation, User Progression Monitoring and Statistics.

- ESL-SOF. EDIBON Student Labsoft (Student Software).

ESL-SOF is the application addressed to the Students that helps them to understand theoretical concepts by means of practical exercises and to prove their knowledge and progression by performing tests and calculations in addition to Multimedia Resources. Default planned tasks and an Open workgroup are provided by EDIBON to allow the students start working from the first session. Reports and statistics are available to know their progression at any time, as well as explanations for every exercise to reinforce the theoretically acquired  technical knowledge.

Innovative features:

• Student Log-In & Self-Registration.

• Existing Tasks checking & Monitoring.

• Default contents & scheduled tasks available to be used from the first session.

• Practical Exercises accomplishment by following the Manual provided by EDIBON.

• Evaluation Methods to prove your knowledge and progression.

• Test self-correction.

• Calculations computing and plotting.

• Equation System Solver Engine.

• User Monitoring Learning & Printable Reports.

• Multimedia-Supported auxiliary resources.