TENDER SPECIFICATIONS

The “AEL-SCIMS” application includes the following elements:

• N-ARR13. Direct Starter with Inversion Module.

Nominal voltage: 400 VAC.

Three input terminals for power supply connection.

Six output terminals for motor connection.

Maximum contacts current: 10 A.

Three position switch:

0: Open circuit.

1: Direct connection.

2: Reverse connection.

• N-VVCA. Advaced AC Motors Speed Controller Module.

Supply voltage: 230 VAC.

Nominal power: 750 W.

Power output terminals: 230 VCA/PWM VAC.

Control panel with digital inputs:

Five configurable digital inputs.

Analog control panel:

0 - 10 V analog input for speed control.

4 - 20 mA analog input for speed control.

10 K potentiometer for the induction motor control speed.

Two relay outputs for alarms configuration:

Two NO/NC outputs.

Two 50 mA transistor outputs.

Setting and visualization of the machine parameters.

• N-ARR01. Manual Star-Delta Starter Module.

Nominal voltage: 400 VAC.

Three input terminals for power supply connection.

Six output terminals for motor connection.

Maximum contacts current: 10 A.

Star-delta three positions commutator:

0: Open circuit.

Y: Star connection.

Δ: Delta connection.

• N-ALI01. Industrial Main Power Supply Module.

Supply voltage: 400 VAC, 3PH + N.

ON/OFF removable key.

Output voltage connections:

Three-phase + Neutral: 400 VAC.

Single-phase: 230 VAC.

Three-phase supply hose with IP44 3PN + E 32 A 400 V connecting plug.

Differential magnetothermal 4 poles, 25 A, 30 mA AC 6 KA.

Emergency stop push-button.

• N-ARR12. Direct Starter Module.

Nominal voltage: 400 VAC.

Three input terminals for power supply connection.

Six output terminals for motor connection.

Maximum contacts current: 10 A.

Two ON/OFF switches:

0: Open circuit.

Y: Closed circuit.

• N-VVCC/M. DC Motor Speed Controller Module (intermediate option).

Supply voltage: 230 VAC.

Variable output voltage: 0 - 300 VDC.

Fuse: 2 A.

• N-TRANS03. Three-phase Autotransformer 400/230 VAC, 1 kVA, Module.

Three-phase autotransformer.

Input voltage: 400 VAC (3PH).

Output voltage: 3 x 230 VAC (3PH + N).

Nominal power: 1 kVA.

Three-phase ON/OFF switch.

Fuses: 3 x 5 A.

• N-EALD. Network Analyzer Module with Oscilloscope and Data Acquisition.

The network analyzer module allows fulfilling measurements, displaying and analyzing all the parameters of the AC electrical networks. It has an LCD screen and push-buttons for the navigation through the different menus. It includes specific software for monitoring current and voltage curves, harmonics display, tariffs programming, alarms programming and electrical parameters storage.

Features:

Multifunctional three-phase power meter:

Three-phase and single-phase voltage. Up to 690 VAC L-L.

Line and neutral nominal current: 10 A.

Active, reactive and apparent power.

Suitable frequencies: 25 Hz, 50 Hz, 60 Hz and 400 Hz.

Display of the V-I vector diagram.

Supply voltage: 85 - 265 VAC.

Energy quality control:

Current and voltage individual harmonics measurement. Up to the 40th harmonic.

Voltage and current THD, TDD and K-Factor.

Maximums and minimums display.

Waveforms display, 128 samples/sec.

Events and data storage:

Harmonics analyzer:

Voltage and current THD, current TDD and K-Factor, up to the 40th harmonic.

Current and voltage harmonic spectrum and angles.

Tariff programming:

Class 0.5S IEC 62053 - 22, active and reactive power in four quadrants.

Measurement of the total and per phase three-phase active, reactive and apparent powers.

Usage time, four energy/demand records of total tariffs.

Eight tariffs, four seasons and four types of days.

Automatic daily report of energy consumption maximums and minimums.

Communications:

RS-485 communication port.

• FRECP. Eddy Current Brake.

Maximum supply voltage: 60 VDC.

Nominal current: 1.67 A.

Maximum current: 1.8 A.

Maximum braking torque: 1.4 Nm.

Shaft height: 71 mm.

• EMT7. 3PH Squirrel-Cage Motor.

Nominal power: 370 W.

Nominal voltage: 3 x 230/400 VAC Δ/Y.

Frequency: 50/60 Hz.

Number of poles: 2.

RPM: 2730 rpm.

Shaft height: 71 mm.

• MED65. Digital Multimeter.

Digital multimeter of about 3 ½ digits, with double-jack ending cables of about 4 mm to facilitate interconnections.

With this digital multimeter we will be able to measure:

Voltage.

Current.

Resistance.

Capacitors capacity.

Temperature.

Additional recommended elements (Not included):

• EM-SCADA. Control and Data Acquisition System Software for Electrical Machines.

Power supply: 230 VAC.

Input signals:

Current signal (x2).

RMS current signal (x2).

Voltage signal (x2).

RMS voltage signal (x2).

Torque and speed signals.

Output signals:

Torque control signal for the servomotor.

Speed control signal for the servomotor.

The three softwares are part of the SCADA system.

Compatible with actual Windows operating systems. Graphic and intuitive simulation of the process in screen. Compatible with the industry standards.

Registration and visualization of all process variables in an automatic and simultaneous way.

Management, processing, comparison and storage of data.

It allows graphic representation in real time.

Comparative analysis of the obtained data, after the process and modification of the conditions during the process.

This unit allows the 30 students of the classroom to visualize simultaneously all the results and the manipulation of the unit, during the process, by using a projector or an electronic whiteboard.

• AEL-SERIN/CA-1KW. 1 kW AC Industrial Servomotor Application.

• N-ALI01. Industrial Main Power Supply Module.

Supply voltage: 400 VAC, 3PH + N.

ON/OFF removable key.

Output voltage connections:

Three-phase + Neutral: 400 VAC.

Single-phase: 230 VAC.

Three-phase supply hose with IP44 3PN + E 32 A 400 V connecting plug.

Differential magnetothermal 4 poles, 25 A, 30 mA AC 6 KA.

Emergency stop push button.

• N-DMC01. Torque and Speed Measurement Module 1.

Digital torque meter:

Torque signal connector.

Auxiliary contact NO.

Digital speed meter:

Speed signal connector.

Auxiliary contact NO.

IP66 protection.

• N-SERV1K. 1 kW Servomotor Module.

Dynamic and static operating regime in four quadrants.

Speed and torque signals.

Power supply terminals: 3 x 400 VAC.

Frequency: 50/60 Hz.

Nominal power: 1 kW.

Maximum power: 3 kW.

Maximum speed: 5000 rpm.

Nominal torque: 3.18 Nm.

Maximum torque: 9.55 Nm.

Temperature control.

Speed control potentiometer.

Torque control potentiometer.

Mode selection switch: torque/speed control.

Motor turning reversal switch.

• All necessary cables to realize the practical exercises are included.

Cables and Accessories, for normal operation.

Manuals:

This unit is supplied with the following manuals: Required Services, Assembly and Installation, Starting-up, Safety, Maintenance & Practices Manuals.

- Dimensions: 1380 x 840 x 2010 mm approx.  (54.33 x 33.07 x 79.13 inches approx.). - Weight: 85 Kg approx. (187 pounds approx.).

EXERCISES AND PRACTICAL POSSIBILITIES

1.- Advanced programming of a variable frequency controller.

2.- Manual control speed of the induction motor with the frequency controller.

3.- Direct and inverse operations with the induction motor and the frequency controller.

4.- Programming of the acceleration time of the induction motor with the frequency controller.

5.- Programming of the deceleration time of the induction motor with the frequency controller.

6.- Programming different conditions with digital inputs in the frequency controller to simulate different real situations in the industry.

7.- Programming the speed response of the induction motor with the frequency controller.

8.- Study of power consumption of the induction motor increasing the braking torque.

9.- Study of different alarms that can be programmed in the frequency controller.

10.- Study of manual star-delta motor starting.

11.- Study of the direct start with motor inversion.

12.- Study of the direct motor starting.

Some practical exercises possibilities with the EM-SCADA and AEL-SERIN/CA-1KW:

13.-  Visualization of torque/current vs speed curves of the induction motor with manual star/delta starter.

14.- Visualization of torque/current vs speed curves of the induction motor with the frequency controller.

15.- Visualization of torque/current vs speed curves of the induction motor with direct starter.

16.- Comparison of graphs with different starting types.

- Several other exercises can be done and designed by the user.

Optional

AEL-SCIMS/ICAI. Interactive Computer Aided Instruction Software:

This complete software package consists of an Instructor Software (EDIBON Classroom Manager - ECM-SOF) totally integrated with the Student Software (EDIBON Student Labsoft - ESL-SOF). Both are interconnected so that the teacher knows at any moment what is the theoretical and practical knowledge of the students.

- ECM-SOF. EDIBON Classroom Manager (Instructor Software).

ECM-SOF is the application that allows the Instructor to register students, manage and assign tasks for workgroups, create own content to carry out Practical Exercises, choose one of the evaluation methods to check the Student knowledge and monitor the progression related to the planned tasks for individual students, workgroups, units, etc... so the teacher can know in real time the level of understanding of any student in the classroom.

Innovative features:

• User Data Base Management.

• Administration and assignment of Workgroup, Task and Training sessions.

• Creation and Integration of Practical Exercises and Multimedia Resources.

• Custom Design of Evaluation Methods.

• Creation and assignment of Formulas & Equations.

• Equation System Solver Engine.

• Updatable Contents.

• Report generation, User Progression Monitoring and Statistics.

- ESL-SOF. EDIBON Student Labsoft (Student Software).

ESL-SOF is the application addressed to the Students that helps them to understand theoretical concepts by means of practical exercises and to prove their knowledge and progression by performing tests and calculations in addition to Multimedia Resources. Default planned tasks and an Open workgroup are provided by EDIBON to allow the students start working from the first session. Reports and statistics are available to know their progression at any time, as well as explanations for every exercise to reinforce the theoretically acquired  technical knowledge.

Innovative features:

• Student Log-In & Self-Registration.

• Existing Tasks checking & Monitoring.

• Default contents & scheduled tasks available to be used from the first session.

• Practical Exercises accomplishment by following the Manual provided by EDIBON.

• Evaluation Methods to prove your knowledge and progression.

• Test self-correction.

• Calculations computing and plotting.

• Equation System Solver Engine.

• User Monitoring Learning & Printable Reports.

• Multimedia-Supported auxiliary resources.