TENDER SPECIFICATIONS

Bench-top unit.

Anodized aluminum frame and panels made of painted steel.

Main metallic elements made of stainless steel.

Vertical position.

Twelve Manometric tubes, length: 500 mm.

Tubes inner diameter: 8 mm, to avoid bubbles.

Air pump for pressurization.

Twelve points for differential pressure measurement, with key.

Common collector.

Non-return valve.

Drain valve.

Millimeter precision rules, length: 500 mm.

Manuals: This unit is supplied with the following manuals: Required services, Assembly and Installation, Starting-up, Safety, Maintenance & Practices manuals.

- Dimensions: 400 x 500 x 870 mm approx. (15.74 x 19.68 x 34.25 inches approx.). - Weight: 5 Kg approx. (11 pounds approx.)