TENDER SPECIFICATIONS

The kit includes:

Manuals.

Set of practice wires.

Switch, two positions.

Five switches, three positions.

Red lamp 12 V.

Button potentiometer 10 K.

Button potentiometer 500 ohms.

Resistance 0 (bridge).

Dos resistances 1.5 K.

Resistance 100 ohms.

Five resistances 10 K.

Resistance 12 K.

Five resistances 1 K.

Five resistances 2.2 K.

Three resistances 2.7 K.

Resistance 33 ohms.

Two resistances 330 ohms.

Four resistances 4.7 K.

Resistance 470 K.

Two resistances 680 ohms.

Required elements (Not included):

- FACO. Power Supply.

- N-M15. Own Development Module.

Additional recommended elements (Not included):

- EDAS/VIS-0.25. EDIBON Data Acquisition System and Virtual Instrumentation (speed: 250,000 samples/s).

or

- EDAS/VIS-1.25. EDIBON Data Acquisition System and Virtual Instrumentation (speed: 1,250,000 samples/s).

Dimensions: 300 x 300 x 200 mm approx. (11.81 x 11.81 x 7.87 inches approx.). Weight: 500 g approx. (1 pound approx.)

EXERCISES AND PRACTICAL POSSIBILITIES

Measurement managing and checking instruments:

1.-  Electronic instrumentation operation. Use of multimeter.

2.-  Faults study of F1 in resistance circuit.

3.-  Faults study of F2 in resistance circuit.

4.-  Theoretical/practical exercises.

Ohm’s Law:

5.-  Ohm’s Law verification.

6.-  Power calculation.

7.-  Theoretical/practical exercises.

Resistors: characteristics and types:

8.-  Resistor measurements.

9.-  Faults study of F1 in resistors circuit.

10.-Faults study of F2 in resistors circuit.

11.-Theoretical/practical exercises.

Resistors association and the Wheatstone bridge:

12.-Voltage and current measurement in a circuit with resistors connected in series.

13.-Parallel configuration study.

14.-The Wheatstone bridge.

15.-Faults study of F1 in series resistors circuit.

16.-Faults study of F2 in parallel resistors circuit.

17.-Faults study of F1 in Wheatstone bridge circuit.

18.-Faults study of F2 in Wheatstone bridge circuit.

19.-Theoretical/practical exercises.

Kirchoff’s laws:

20.-Kirchoff’s first law.

21.-Kirchoff’s second law.

22.-Fault study using Kirchoff’s law.

23.-Theoretical/practical exercises.

Additional practical possibilities:

24.-Voltage/current dividers.

25.-Batteries and switches.

26.-Power source in series and parallel.

27.-The rheostat and potentiometer.

-Several other exercises can be done and designed by the user.

Optional

M1/KIT/ICAI. Interactive Computer Aided Instruction Software:

This complete software package consists of an Instructor Software (EDIBON Classroom Manager - ECM-SOF) totally integrated with the Student Software (EDIBON Student Labsoft - ESL-SOF). Both are interconnected so that the teacher knows at any moment what is the theoretical and practical knowledge of the students.

- ECM-SOF. EDIBON Classroom Manager (Instructor Software).

ECM-SOF is the application that allows the Instructor to register students, manage and assign tasks for workgroups, create own content to carry out Practical Exercises, choose one of the evaluation methods to check the Student knowledge and monitor the progression related to the planned tasks for individual students, workgroups, units, etc... so the teacher can know in real time the level of understanding of any student in the classroom.

Innovative features:

• User Data Base Management.

• Administration and assignment of Workgroup, Task and Training sessions.

• Creation and Integration of Practical Exercises and Multimedia Resources.

• Custom Design of Evaluation Methods.

• Creation and assignment of Formulas & Equations.

• Equation System Solver Engine.

• Updatable Contents.

• Report generation, User Progression Monitoring and Statistics.

- ESL-SOF. EDIBON Student Labsoft (Student Software).

ESL-SOF is the application addressed to the Students that helps them to understand theoretical concepts by means of practical exercises and to prove their knowledge and progression by performing tests and calculations in addition to Multimedia Resources. Default planned tasks and an Open workgroup are provided by EDIBON to allow the students start working from the first session. Reports and statistics are available to know their progression at any time, as well as explanations for every exercise to reinforce the theoretically acquired  technical knowledge.

Innovative features:

• Student Log-In & Self-Registration.

• Existing Tasks checking & Monitoring.

• Default contents & scheduled tasks available to be used from the first session.

• Practical Exercises accomplishment by following the Manual provided by EDIBON.

• Evaluation Methods to prove your knowledge and progression.

• Test self-correction.

• Calculations computing and plotting.

• Equation System Solver Engine.

• User Monitoring Learning & Printable Reports.

• Multimedia-Supported auxiliary resources.