TENDER SPECIFICATIONS

Bench-top unit.

Anodized aluminum frame and panels made of painted steel.

Main metallic elements made of stainless steel.

The “MARP” unit mainly consists of:

Frame with measurement system to level the ends of the parabolic arch.

Parabolic arch made of tempered steel with seven cords with hangers to hang the weights from them (uniformly distributed load or point load):

Length: 500 mm.

Height: 200 mm.

Cross section: 20 x 1.5 mm.

Support systems:

Fixed end.

Movable end that moves horizontally along a guide. This end can be transformed into a fixed end.

Three pairs of pulleys that allow to lodge the weights required for:

To cancel out the horizontal displacement and to fix the movable support.

To compensate the vertical reaction of the support.

Two dial gauges:

Range:  0 – 25 mm.

Precision: 0.01 mm.

Set of weights:

Weights to apply load on the parabolic arch:

7 hangers of 100 gr.

7 weights of 100 gr.

7 weights of 50 gr.

Weights to compensate the reactions in the fixed support:

4 hangers of 100 gr.

13 weights of 100 gr.

13 weights of 50 gr.

Storage cage, with packing foam, for the weights and hangers.

Manuals: This unit is supplied with the following manuals: Required services, Assembly and Installation, Starting-up, Security, Maintenance and Practices manual.

Unit:  - Dimensions: 850 x 400 x 700 mm approx. (33.46 x 15.74 x 27.56 inches approx.)  - Weight: 30 Kg approx. (154.3 pounds approx.).

Storage case for the weights and hangers: - Dimensions: 350 x 300 x 150 mm approx. (13.78 x 11.81 x 5.9 inches approx.)  - Weight: 5 Kg approx. (11 pounds approx.).

EXERCISES AND PRACTICAL POSSIBILITIES

1.- Study of the mechanical principles of a parabolic arch.

2.- Differences between an isostatic arch and a hyperstatic arch.

3.- Analysis of the arch under load:

Measurement of the deformations.

Measurement of the reactions of the supports in the hyperstatic arch.

4.- Influence of a point load or an evenly distributed load on the reactions at the support and on the deformation of the arch.

5.- Evaluation of the relation between applied load and horizontal displacement.

6.- Comparison of the horizontal displacement with theoretical values.

7.- Analysis of the horizontal thrust.

Optional

MARP/ICAI. Interactive Computer Aided Instruction Software:

This complete software package consists of an Instructor Software (EDIBON Classroom Manager - ECM-SOF) totally integrated with the Student Software (EDIBON Student Labsoft - ESL-SOF). Both are interconnected so that the teacher knows at any moment what is the theoretical and practical knowledge of the students.

- ECM-SOF. EDIBON Classroom Manager (Instructor Software).

ECM-SOF is the application that allows the Instructor to register students, manage and assign tasks for workgroups, create own content to carry out Practical Exercises, choose one of the evaluation methods to check the Student knowledge and monitor the progression related to the planned tasks for individual students, workgroups, units, etc... so the teacher can know in real time the level of understanding of any student in the classroom.

Innovative features:

• User Data Base Management.

• Administration and assignment of Workgroup, Task and Training sessions.

• Creation and Integration of Practical Exercises and Multimedia Resources.

• Custom Design of Evaluation Methods.

• Creation and assignment of Formulas & Equations.

• Equation System Solver Engine.

• Updatable Contents.

• Report generation, User Progression Monitoring and Statistics.

- ESL-SOF. EDIBON Student Labsoft (Student Software).

ESL-SOF is the application addressed to the Students that helps them to understand theoretical concepts by means of practical exercises and to prove their knowledge and progression by performing tests and calculations in addition to Multimedia Resources. Default planned tasks and an Open workgroup are provided by EDIBON to allow the students start working from the first session. Reports and statistics are available to know their progression at any time, as well as explanations for every exercise to reinforce the theoretically acquired  technical knowledge.

Innovative features:

• Student Log-In & Self-Registration.

• Existing Tasks checking & Monitoring.

• Default contents & scheduled tasks available to be used from the first session.

• Practical Exercises accomplishment by following the Manual provided by EDIBON.

• Evaluation Methods to prove your knowledge and progression.

• Test self-correction.

• Calculations computing and plotting.

• Equation System Solver Engine.

• User Monitoring Learning & Printable Reports.

• Multimedia-Supported auxiliary resources.