TENDER SPECIFICATIONS (for main items)

1 PBGC/CTS Unit:

Anodized aluminum frame and panels made of painted steel.

The unit includes wheels to facilitate its mobility.

Main metallic elements made of stainless steel.

Diagram in the front panel with distribution of the elements similar to the real one.

Supply tank made of stainless steel. Capacity: 25  l. It includes:

Agitator made of stainless steel. Max. speed: 200 rpm.

Sight glass.

Three computer controlled pumps to impel the substrate. Max. flow rate: 25  l/h.

Two reactors made of stainless steel. Capacity: between 20  l – 70  l. Each reactor includes:

Level sensor.

“J“ type temperature sensor.

pH sensor, range: 0 – 14.

Agitator made of stainless steel. Max. speed: 150 rpm.

Heating jacket.

Sight glass.

Digestate collection tank made of stainless steel. Capacity: 25  l. It includes:

Level sensor.

Sight glass.

pH adjustment system:

Two computer controlled peristaltic pumps to impel the acid and base. Max. flow rate: 2.5  l/h.

Two tanks for the acid and the base made of polypropylene. Capacity: 5  l each.

Heating system consisting of:

Tank made of stainless steel equipped with:

Computer controlled electric heating element. Temperature PID control.

“J“ type temperature sensor to measure the water temperature.

Level switch to control the water level in the tank.

Cover made of stainless steel to avoid contact with hot water. It includes an orifice to observe the level of water and, even, to refill the tank.

Valve to drain water.

Pump to impel hot water. Max. flow rate: 8  l/min.

Silica gel column for biogas drying.

Valves to select the circuits.

Sampling point with valve for external sampling of generated biogas.

Biogas analysis section:

Sensor to measure the methane concentration of the generated biogas, 0 – 100 %.

Sensor to measure the carbon dioxide concentration of the generated biogas, 0 – 100 %.

“J“ type temperature sensor.

Humidity sensor, 0 – 100 %.

Sensor to measure the flow rate of generated biogas, range: 0 – 30 Nl/h.

Computer and touch screen control: PLC controller to control the unit locally.

The complete unit includes as well:

Computer and touch screen control: PLC controller to control the unit locally.

The complete unit includes as well:

Advanced Real-Time SCADA and PID Control.

Open Control + Multicontrol + Real-Time Control.

Specialized EDIBON Control Software based on LabVIEW.

National Instruments Data Acquisition board (250 KS/s, kilo samples per second).

Calibration exercises, which are included, teach the user how to calibrate a sensor and the importance of checking the accuracy of the sensors before taking measurements.

Projector and/or electronic whiteboard compatibility allows the unit to be explained and demonstrated to an entire class at one time.

Capable of doing applied research, real industrial simulation, training courses, etc.

Remote operation and control by the user and remote control for EDIBON technical support, are always included.

Totally safe, utilizing 4 safety systems (Mechanical, Electrical, Electronic & Software).

Designed and manufactured under several quality standards.

Optional ICAI software to create, edit and carry out practical exercises, tests, exams, calculations, etc. Apart from monitoring user's knowledge and progress reached.

This unit has been designed for future expansion and integration. A common expansion is the EDIBON Scada-Net (ESN) System which enables multiple students to simultaneously operate many units in a network.

2 PBGC/CTS/CCSOF. PID Computer Control +Data Acquisition+Data Management Software:

The three softwares are part of the SCADA system.

Compatible with the industry standards.

Flexible, open and multicontrol software, developed with actual windows graphic systems, acting simultaneously on all process parameters.

Analog and digital PID control. PID menu and set point selection required in the whole work range.

Management, processing, comparison and storage of data.

Sampling velocity up to 250 KS/s (kilo samples per second).

Calibration system for the sensors involved in the process.

It allows the registration of the alarms state and the graphic representation in real time.

Open software, allowing the teacher to modify texts, instructions. Teacher’s and student’s passwords to facilitate the teacher’s control on the student, and allowing the access to different work levels.

This unit allows the 30 students of the classroom to visualize simultaneously all the results and the manipulation of the unit, during the process, by using a projector or an electronic whiteboard.

3 Cables and Accessories, for normal operation.

4 Manuals:

This unit is supplied with 8 manuals: Required Services, Assembly and Installation, Control Software, Starting-up, Safety, Maintenance, Calibration & Practices Manuals.

*	References 1 to 4 are the main items: PBGC/CTS + PBGC/CTS/CCSOF + Cables and Accessories + Manuals are included in the minimum supply for enabling normal and full operation.

EXERCISES AND PRACTICAL POSSIBILITIES TO BE DONE WITH THE MAIN ITEMS

1.-  Study of the stabilization process.

2.-  Study of the effect of temperature on the anaerobic digestion, purification and quality of the obtained biogas.

3.-  Study of the pH effect on the anaerobic digestion, purification and quality of the obtained biogas.

4.-  Study of the volumetric load influence on the anaerobic digestion, purification and quality of the obtained biogas.

5.-  Study of the type of substrate influence on the anaerobic digestion, purification and quality of the obtained biogas.

6.-  Study of the inhibitors influence on the anaerobic digestion, purification and quality of the obtained biogas.

7.-  Influence of the working mode, with one or two stages, on the generation of biogas.

8.-  Influence of the working mode, continuous or batch, on the generation of biogas.

9.-  Influence of the working mode, with or without prior fermentation, on the generation of biogas.

10.-Determination of the optimum operation temperature.

11.-Determination of the optimum feeding rate.

12.-Determination of the flow rate, output and quality of biogas under different working conditions.

Additional practical possibilities:

13.-Sensors calibration.

Other possibilities to be done with this unit:

14.- Many students view results simultaneously.

To view all results in real time in the classroom by means of a projector or an electronic whiteboard.

15.- Open Control, Multicontrol and Real Time Control.

This unit allows intrinsically and/or extrinsically to change the span, gains; proportional, integral, derivative parameters; etc, in real time.

16.- The Computer Control System with SCADA and PID Control allow a real industrial simulation.

17.- This unit is totally safe as uses mechanical, electrical/electronic, and software safety devices.

18.- This unit can be used for doing applied research.

19.- This unit can be used for giving training courses to Industries even to other Technical Education Institutions.

20.- Visualization of all the sensors values used in the PBGC/CTS unit process.

- Several other exercises can be done and designed by the user.

TENDER SPECIFICATIONS (for optional items)

a) Technical and Vocational Education configuration

5 PBGC/CTS/ICAI. Interactive Computer Aided Instruction Software.

This complete software package consists of an Instructor Software (EDIBON Classroom Manager - ECM-SOF) totally integrated with the Student Software (EDIBON Student Labsoft - ESL-SOF). Both are interconnected so that the teacher knows at any moment what is the theoretical and practical knowledge of the students.

- ECM-SOF. EDIBON Classroom Manager (Instructor Software).

ECM-SOF is the application that allows the Instructor to register students, manage and assign tasks for workgroups, create own content to carry out Practical Exercises, choose one of the evaluation methods to check the Student knowledge and monitor the progression related to the planned tasks for individual students, workgroups, units, etc...so the teacher can know in real time the level of understanding of any student in the classroom.

Innovative features:

• User Data Base Management.

• Administration and assignment of Workgroup, Task and Training sessions.

• Creation and Integration of Practical Exercises and Multimedia Resources.

• Custom Design of Evaluation Methods.

• Creation and assignment of Formulas & Equations.

• Equation System Solver Engine.

• Updatable Contents.

• Report generation, User Progression Monitoring and Statistics.

- ESL-SOF. EDIBON Student Labsoft (Student Software).

ESL-SOF is the application addressed to the Students that helps them to understand theoretical concepts by means of practical exercises and to prove their knowledge and progression by performing tests and calculations in addition to Multimedia Resources. Default planned tasks and an Open workgroup are provided by EDIBON to allow the students start working from the first session. Reports and statistics are available to know their progression at any time, as well as explanations for every exercise to reinforce the theoretically acquired technical knowledge.

Innovative features:

• Student Log-In & Self-Registration.

• Existing Tasks checking & Monitoring.

• Default contents & scheduled tasks available to be used from the first session.

• Practical Exercises accomplishment by following the Manual provided by EDIBON.

• Evaluation Methods to prove your knowledge and progression.

• Test self-correction.

• Calculations computing and plotting.

• Equation System Solver Engine.

• User Monitoring Learning & Printable Reports.

• Multimedia-Supported auxiliary resources.

b) Multipost Expansions options

6 MINI ESN. EDIBON Mini Scada-Net System for being used with EDIBON Teaching Units.

MINI ESN. EDIBON Mini Scada-Net System allows up to 30 students to work with a Teaching Unit in any laboratory, simultaneously.

The MINI ESN system consists of the adaptation of any EDIBON Computer Controlled Unit with SCADA and PID Control integrated in a local network.

This system allows to view/control the unit remotely, from any computer integrated in the local net (in the classroom), through the main computer connected to the unit.

Main characteristics:

- It allows up to 30 students to work simultaneously with the EDIBON Computer Controlled Unit with SCADA and PID Control, connected in a local net.

- Open Control + Multicontrol + Real Time Control + Multi Student Post.

- Instructor controls and explains to all students at the same time.

- Any user/student can work doing "real time" control/multicontrol and visualisation.

- Instructor can see in the computer what any user/student is doing in the unit.

- Continuous communication between the instructor and all the users/students connected.

Main advantages:

- It allows an easier and quicker understanding.

- This system allows you can save time and cost.

- Future expansions with more EDIBON Units.

The system basically will consist of:

This system is used with a Computer Controlled Unit.

- Instructor’s computer.

- Students’ computers.

- Local Network.

- Unit-Control Interface adaptation.

- Unit Software adaptation.

- Webcam.

- MINI ESN Software to control the whole system.

- Cables and accessories required for a normal operation.