TENDER SPECIFICATIONS

Structure made of painted iron.

The unit includes wheels to facilitate its mobility.

Diagram in the front panel with distribution of the elements similar to the real one.

The main elements of the unit are thermally insulated.

Heat pump:

Flow rate: 3.1 m³/h.

Heating power range: 1.62 – 7.33 KW.

Electric power range: 0.15 – 1.17 kW.

COP range: 11.04 – 6.3.

Fan speed: 600 – 700 rpm (400 rpm quiet mode).

Pump:

Type: dosing pump.

Maximum flow rate: 4.8 m³/h.

Maximum pressure: 2.2 bar.

Power: 0.37 kW.

Tank:

Volume: 100 l.

Material: vitrified internally.

Instrumentation:

Set of six manual globe valves.

One manual globe valve for drainage.

One manual valve for venting.

One level sensor.

Cables and accessories, for normal operation.

Manual:

This unit is supplied whit the following operation manual: Required services, Assembly and Installation, Starting-up, Safety, Maintenance & Practices manuals.

-Dimensions: 1245 x 770 x 1210 mm approx. (49.21 x 31.49 x 45.27 inches approx.) - Weight (without load): 150 kg approx. (330.6 inches approx.)

- Weight (loaded): 250 kg approx. (551.1 inches approx.)