TENDER SPECIFICATIONS

The “WIT-MDRV” application includes the following elements:

• TRANS03. Three-phase Autotransformer 400/230 VAC, 1 kVA.

Three-phase autotransformer.

Nominal supply voltage: 400 VAC (3PH).

Nominal output voltage: 3 x 230 VAC (3PH + N).

Nominal power: 1 kVA.

Transformer connection: YY0.

• FP-ESS. Electronic Soft Starter.

Nominal voltage: 400 VAC.

Nominal current: 3.6 A.

Nominal power: 1.5 kW.

Protection index: IP20.

Three-phase.

Regulating potentiometer for setting the acceleration/deceleration ramp.

Regulating potentiometer for starting voltage.

• FP-KIT-7. Manual Starters for Three-Phase Induction Motor of Squirrel Cage Kit.

Manual star-delta starter:

Nominal voltage: 400 VAC.

Maximum current contacts: 10 A.

Star-delta three position commutator:

0: Open circuit.

Y: Star connection.

Δ: Delta connection.

Direct manual starter:

Nominal voltage: 400 VAC.

Maximum current contacts: 10 A.

Two positions commutator (ON/OFF):

0: Open.

1: Close.

Manual direct starter with inversión:

Nominal voltage: 400 VAC.

Maximum current contacts: 10 A.

Three positions commutator:

0: Open.

1: Direct connection.

2: Inverse connection.

• FP-KIT-3. AC Motor Controller Installation Kit.

Frequency controller:

Supply voltage: 230 VAC.

Nominal power: 0.4 kW.

PWM output voltage connections:

Three-phases: 230 VAC.

Potentiometer for the induction motor control speed.

Setting and visualization display of the machine parameters.

EMC/EMI filter to limit electromagnetic interference.

Potentiometer.

Control cabinet with door:

Dimensions:

Height: 500 mm.

Width: 400 mm.

Depth: 200 mm.

• EMT7-E. 3PH Squirrel-Cage Industrial Motor.

Nominal power: 370 W.

Nominal voltage: 3 x 230/400 V AC Δ/Y.

Frequency: 50/60 Hz.

Number of poles: 2.

Speed: 2730 rpm.

Nominal current: 1.67/ 0.97 A.

Shaft height: 71 mm.

• FP-KIT-2. DC Motor Controller Installation Kit.

DC motor controller:

Supply voltage: 230 VAC (PH + N).

Three ON/OFF switches:

ON/OFF power switch.

Start-stop control activation switch.

Internal tacho dynamo feedback switch.

Two potentiometers:

Speed control.

Torque control.

Terminals:

Rotor terminals.

Excitation terminals.

Tacho dynamo terminals.

Three driver status leds (red, yellow and green).

Variable output voltage: 0 – 300 VDC.

A control cabinet with door:

Dimensions:

Height: 500 mm.

Width: 400 mm.

Depth: 200 mm.

2 m cut rail bar.

2 m grey duct bar for wiring.

200 W, DC motor with wound rotor.

• EMT5-E. DC Shunt/Series/Compound Excitation Industrial Motor-Generator.

Nominal power: 300 W.

Armature voltage: 200 VDC.

Excitation voltage: 230 VDC.

Armature current: 1.5 A.

Excitation current: 0.4 A.

Speed: 3400/7500 rpm.

Shaft height: 71 mm.

• FP-KIT-6. Signaling and Control Kit.

Three commutators:

Two positions commutator.

Three signalling lamps:

Nominal voltage: 230 VAC.

Three lamps (red, yellow and green).

Emergency stop push-button (230/400 VAC):

Supply voltage: 230/400 VAC.

• MED65. Digital Multimeter.

This module has a digital multimeter of 3 ½ digits, with double-jack ending cables of about 4 mm to facilitate interconnections.

With this digital multimeter we will be able to measure:

Voltage.

Current.

Resistance.

Capacitors capacity.

Temperature.

• CHER. Tool Box.

Crimper.

Tin.

Meter.

Insulating tape.

Heat shrink.

Pin punch.

Star and flat screwdrivers.

Allen keys.

Soldering iron and soldering iron support.

Rubber hammer.

Connection terminals.

Cable ties.

Cable cutters.

Clamps.

• FP-KIT-10. Tubes and Fittings for Channeling Wiring Kit.

5 meters of PVC pipe for wiring installation.

Three electrical boxes.

Cable guide.

20 x Cable clamps, 20 mm.

• FP-KIT-4. Wiring Installation Kit.

100 m of grey wire of 1.5 mm².

100 m of brown wire of 1.5 mm².

100 m of black wire of 1.5 mm².

100 m of green/yellow wire of de 1.5 mm².

25 m of screened wire.

• FP-STR. Assembly Frame with Safe Electrical Power Supply.

Aluminium structure:

Two aluminium struts.

Easy assembly of components via hammer head screws.

Possibility of simultaneous  work of several students.

Four swivelling casters to facilitate the movement.

Dimensions:

Structure heigh: 1800 mm.

Useful working height: 1000 mm.

Width: 1500 mm.

Three-phase connection plug.

Safe electric box:

Differential magnetothermal, 4 poles, 25 A, 300 mA AC 6 kA.

Emergency stop mushroom (230/400 VAC).

5-wire hose for connection to frame.

Signal lamp of voltage presence.

• FP-KIT-1. Feeders Installation Kit.

Differential magnetothermal 4 poles, 25 A, 30 mA AC 6 KA.

Single-phase fuse holder for DIN rail mounting:

Fuse: 1 x 30 A.

Three-phase fuse holder for DIN rail mounting:

Fuses: 3 x 30 A.

Recommended additional elements (Not included):

• FP-KIT-5. Measuring Kit.

Clamp meter:

Clamp for alternating/direct current measurements contactless.

The clamp can measure:

Current.

Voltage.

Resistance.

A voltage and continuity tester:

Voltage range: 12 – 690 VAC.

Phases rotating detection in three-phase systems.

Polarity tester.

• FP-KIT-8. PLC Installation and programming Kit.

PLC:

Contacts:

Eight digital inputs.

Four relay outputs.

Software for the PLC programming is included.

8 x control switches.

4 x relays (230 VAC, 2 NC, 2 NO).

• FP-KIT-9. 400 VAC Circuit Breakers Kit.

Five three-pole circuit breakers:

Nominal voltage of power contacts: 400 VAC.

Nominal voltage of control contacts: 230 VAC.

Nominal voltage coil control: 230 VAC.

Auxiliary contacts: 3 NO / 2 NC.

• FP-DLT. Delay Timer.

Nominal voltage: 400 VAC.

Supply voltage: 24 V.

Potentiometers to adjust:

Starting time.

Starting voltage.

Stop time.

• All necessary cables to realize the practical exercises are included.

Cables and accessories, for normal operation.

Manuals:

This unit is supplied with the following manuals: Required services, Assembly and Installation, Starting-up, Safety, Maintenance & Practices manuals.

- Dimensions: 2000 x 400 x 2000 mm approx. (78.74 x 15.75 x 78.74 inches approx.) - Weight: 100 Kg approx. (220 pounds approx.)

EXERCISES AND PRACTICAL POSSIBILITIES

1.- Components and electrical devices installation in the electrical cabinet.

2.- Wiring of the main distribution to the electrical cabinet.

3.- Wiring of AC frequency controller, electrical protections and power and control circuits.

4.- Programming and commissioning of frequency controller.

5.- Programming of acceleration time with the frequency controller.

6.- Programming of deceleration time with the frequency controller.

7.- Frequency/speed control with the AC frequency controller.

8.- Wiring of electronic soft starter for motors.

9.- Configuration and commissioning of electronic soft starter for AC motors.

10.- Wiring of DC motor controller.

11.- Wiring of DC motor to the DC motor controller.

12.- Torque/speed control of the DC motor with the DC controller.

13.- Wiring of AC motor manual starters.

14.- Wiring of the PLC to the frequency controller for maneuvers automation (recommended).

15.- Programming of the PLC according to the requirements of the installation (recommended).

- Several other exercises can be done and designed by the user.

Optional

WIT-MDRV/ICAI. Interactive Computer Aided Instruction Software:

This complete software package consists of an Instructor Software (EDIBON Classroom Manager - ECM-SOF) totally integrated with the Student Software (EDIBON Student Labsoft - ESL-SOF). Both are interconnected so that the teacher knows at any moment what is the theoretical and practical knowledge of the students.

- ECM-SOF. EDIBON Classroom Manager (Instructor Software).

ECM-SOF is the application that allows the Instructor to register students, manage and assign tasks for workgroups, create own content to carry out Practical Exercises, choose one of the evaluation methods to check the Student knowledge and monitor the progression related to the planned tasks for individual students, workgroups, units, etc... so the teacher can know in real time the level of understanding of any student in the classroom.

Innovative features:

• User Data Base Management.

• Administration and assignment of Workgroup, Task and Training sessions.

• Creation and Integration of Practical Exercises and Multimedia Resources.

• Custom Design of Evaluation Methods.

• Creation and assignment of Formulas & Equations.

• Equation System Solver Engine.

• Updatable Contents.

• Report generation, User Progression Monitoring and Statistics.

- ESL-SOF. EDIBON Student Labsoft (Student Software).

ESL-SOF is the application addressed to the Students that helps them to understand theoretical concepts by means of practical exercises and to prove their knowledge and progression by performing tests and calculations in addition to Multimedia Resources. Default planned tasks and an Open workgroup are provided by EDIBON to allow the students start working from the first session. Reports and statistics are available to know their progression at any time, as well as explanations for every exercise to reinforce the theoretically acquired  technical knowledge.

Innovative features:

• Student Log-In & Self-Registration.

• Existing Tasks checking & Monitoring.

• Default contents & scheduled tasks available to be used from the first session.

• Practical Exercises accomplishment by following the Manual provided by EDIBON.

• Evaluation Methods to prove your knowledge and progression.

• Test self-correction.

• Calculations computing and plotting.

• Equation System Solver Engine.

• User Monitoring Learning & Printable Reports.

• Multimedia-Supported auxiliary resources.